## Slide 1
Torsten Brockhaus
Damilare Osunleke
Aleksei Trikoz
Application Project:
Dangerous good classification for the LHG

## Slide 2: l. Contents
1. The task
2. The data
2.1 Raw data
2.2 Labeling
2.3 Sample
The model
    3.1 YOLOv5
    3.2 Training
    3.3 Results
Deployment
Recommendations and next steps

## Slide 3: The task:
Train a ML solution to classify dangerous goods labels on trucks and deploy it in a Docker container.

## Slide 4: The data
Six terabytes of data in total
Stored in four folders, one for each gate
One zip folder for each truck that passed the gate
About forty photos for a single truck
Only the images of the back of the trucks were used
In total, we collected a sample of 338.00 images, of which we examined 70.000 manually
Raw data

## Slide 5: The data
Labeling

## Slide 6: The data
Of the 70,000 images, 2.470 images have atleast one sign
Sample is heavily unbalanced
Consists of images of different times of day with different lighting
Sample

## Slide 7: The model
Acronym for "You only look once“
The first model was developed in 2015 by Redmon et al
Version 5 published in 2020
Can predict multiple bounding boxes and class probabilities
Provides high speed and processes images in real time with minimal latency
Pre-trained on COCO dataset
Can be fine-tuned with user-defined datasets
Built-in image augmentation
YOLOv5

## Slide 8: The model
Of the 2,470 images, 2,270 were used for training and 200 for testing
265 images without sings were added to reduce false positives
Training requires powerful hardware, especially GPUs
Due to the lack of powerful hardware, the training was performed on Google Colab
Google Colab provides limited access to powerful CPUs, GPUs, and RAM
For 100 epochs in 16 batches, the total runtime in Google Colab was about 3.5 hours.
Training

## Slide 9: The model
Training results
Increasing the epochs to 200 did not significantly improve the model's performance.

## Slide 10: The model
Test results
Class | Instances | Precision | Recall | mAP50 | mAP50-95
all | 135 | 0.902 | 0.915 | 0.951 | 0.793
2 Gases | 8 | 0.807 | 0.75 | 0.781 | 0.723
3 Flammable liquids | 23 | 0.876 | 1 | 0.976 | 0.782
5 Oxidizing substances | 5 | 0.962 | 1 | 0.995 | 0.906
6 Toxic substances | 3 | 1 | 0.778 | 0.995 | 0.764
8 Corrosive substances | 19 | 0.896 | 0.905 | 0.964 | 0.771
9 Miscellaneous dangerous | 28 | 0.923 | 1 | 0.988 | 0.815
MP Marine pollutant | 31 | 0.935 | 1 | 0.995 | 0.844
LQ | 18 | 0.82 | 0.889 | 0.917 | 0.741

## Slide 11: The model
Test results

## Slide 12: The model
Examples

## Slide 13: Deployment
Model deployment
The BentoML platform was used for the deployment
The model was containerized as a Docker image (5.92 GB)
Can be downloaded and run on local machines

## Slide 14: Recommendations and next steps
The recommendations below are based on the outcome of the project:
Adopt this model for identifying dangerous goods labels on trucks.
In the meantime, perform second-level checks when label 2 is detected. This is due to relatively low recall for that class and its misidentification as label 3.
Retrain the model, but split label 2 into its constituent sub-labels before training
Integrate the model with the existing booking data from the LHG logistics system for auto verification

## Slide 15: Image sources
(1)https://www.fh-kiel.de/typo3conf/ext/fh_kiel/Resources/Public/Images/News/fachhhochschule-kiel-campus-ecke.jpg
(2) https://www.lubbers.net/wp-content/uploads/2022/06/ADR.png

## Slide 16: Backup
Dangerous goods labels

## Slide 17: Backup
Service APIs